## Slide 1: VPN

## Slide 2: Outline
Intro to VPN.
Types.
Ways to Implement VPN.

## Slide 3: VPN
A virtual private network (VPN) extends a private network across a public network, and enables users to send and receive data across shared or public networks as if their computing devices were directly connected to the private network.
Applications running across a VPN may therefore benefit from the functionality, security, and management of the private network.
Encryption is a common though not an inherent part of a VPN connection.

## Slide 4: VPN
VPN technology was developed to allow remote users and branch offices to access corporate applications and resources. To ensure security, the private network connection is established using an encrypted layered tunnelling protocol and VPN users use authentication methods, including passwords or certificates, to gain access to the VPN.

## Slide 5: Types
Types of VPN: Site- to- Site VPN and Remote- access VPN.
Site- to- Site VPN: Allow a company to connect its remote sites to the corporate backbone securely over internet.
Remote- Access VPN: Allow remote user like telecommuters to securely access the corporate network wherever and they need to.

## Slide 6: Cont..
Security over Internet: VPN uses IPsec to provide secure communication over internet.
Allow for secure data transmission over an IP- based network.
Data confidentiality.
Data integrity.
Data origin authentication.

## Slide 7: Ways to Implement VPN
Three ways to implement VPN:
Generic Routing Encapsulation (GRE): Peer to Peer, No encryption, Manual Tunnel, Not Scalable, Static IP on all End Points.
Dynamic Multi- point VPN (DMVPN): Multi point, uses NHRP(Next Hop Resolution Protocol) protocol.
IPSec: Provides encryption, confidentiality, data integrity, authentication, replay detection.

## Slide 8: Cont..
DMVPN:
Automatically creates VPN tunnels when dynamic IP address on the both ends are used.
Keeping cost low, minimising configuration complexity and increasing flexibility.
NHRP: Maintains tunnel end point IP address with their public IP Address.

## Slide 9: Cont..
IPSec VPN:
Allow two or more hosts to communicate in a secure manner by authenticating and encryption each IP packet of a communication session.
Provides confidentiality, data integrity, authentication, replay detection.
Virtual tunnel between two endpoints.

## Slide 10: Cont..
VPN client packet into VPN server.
VPN gave a secure way to connect to a company’s intranet.
Information between VPN server and the destination server are subjected to normal internet traffic rules.
Open VPN, IKEv2(Microsoft & Cisco)
VPN server needs to know where data is going and who to send it to.

## Slide 11: VPN vs Proxy
SI. | VPN | Proxy
1. | VPN ensures encryption, authentication and integrity protection. | Proxy does not ensure or provide any security.
2. | Protocols used in VPN are PTTP (Point to point tunneling protocol), L2TP (Layer 2 tunneling protocol) etc. | Protocols used in Proxy are FTP, SMTP, HTTP etc.
3. | VPN works on firewall. | Proxy works on browsers.
4. | VPN stands for Virtual Private Network. It simulate a private network over public network. | It does not simulate a private network over public network.
5. | VPN does not hide the IP address of client. | Proxy uses the anonymous network ID instead of actual IP address of client
6. | VPN creates tunnel between end users. | But proxy does not create tunnel between end users.
7. | VPN offers high amount of security. | Proxy does not offer any type of security.
8. | VPN provides seamless and stable connection | Proxy connection is highly unstable.